## Slide 1: Health Care Waste Management

## Slide 2: Learning Objectives
Describe the various types of waste in health care.
Outline the sources that result in health-care waste.
Segregate the healthcare waste appropriately.
List the options for waste treatment.

## Slide 3: Time involved
40 minutes

## Slide 4: Key Points
Sharps most likely health care waste to cause injury and/or exposure
At a minimum, a waste management program must focus on sharps handling
Proper segregation using available means will reduce the risk of disease transmission and minimise the amount of waste generated
A range of treatment options for waste are available
  Consideration should be given to those that reduce the opportunity for exposure and impact on the environment
Education/training, support, supervision and regular reinforcement of practices are the keys to success

## Slide 5: Introduction
Proper management of health care waste creates a safer environment for staff, solid waste workers, and the public
Health care waste management is dictated by
  professional standards
  local laws and national legislation
  available resources
Notes: Health-care activities inevitably generate healthcare waste. Poor management of healthcare waste exposes healthcare workers, waste handlers and the community to infections, toxic effects and injuries.
Of the total amount of waste generated by health-care activities, about 80% is general waste. The remaining 20% is considered hazardous material that may be infectious, toxic or radioactive. Every year an estimated 16,000 million injections are administered worldwide, but not all of the needles and syringes are properly disposed of afterwards.
Infection prevention and control staff must use their experience and understanding of the chain of infection when developing a practical approach to waste management. If one focuses on the true risks of healthcare waste, a safe and effective program can be achieved, even where resources are limited.

## Slide 6: Types of Healthcare Waste
Sharps waste
Infectious waste
Pathological waste
Radioactive waste

## Slide 7: Definitions - 1
Type of Waste | Definition | Examples
Sharps waste | Used or unused sharp items | Auto-disable syringes Broken glass Hypodermic, intravenous, or other needles Infusion sets Knives Pipettes Scalpels Syringes with attached needles
Infectious waste | Waste suspected to contain pathogens | Excreta Laboratory cultures Tissues (swabs), materials, or equipment that have been in contact with infected patients Waste contaminated with blood and other body fluids Waste from isolation wards
Notes: Healthcare waste can be considered any waste generated in a health care setting. Most concern is focused on the hazardous aspect of waste, i.e., infectious, chemical, radioactive, or other waste.
In addition to sharps and pathological waste, infectious waste includes:
  Microbiological waste - culture plates, growth media, etc.
  Swabs, dressings, bandages contaminated with potentially infectious fluids.
  Blood – tubes of blood, units of blood, blood and blood products, and other containers used to collect blood.
The World Health Organization estimates that, in 2000, injections with contaminated syringes caused 21 million hepatitis B virus infections, two million hepatitis C virus infections and 260,000 HIV infections worldwide. Many of these infections were avoidable if the syringes had been disposed of safely.

## Slide 8: Definitions - 2
Type of Waste | Definition | Examples
Pathological waste | Pathological waste | Body parts Fetuses Human tissues, organs or fluids
Pharmaceutical waste, including cytotoxic waste | Pharmaceuticals that are expired or no longer needed | Cytotoxic waste containing substances with genotoxic properties, e.g., waste containing cytostatic drugs (often used in cancer therapy) Genotoxic chemicals Items contaminated by or containing pharmaceuticals
Non-risk general waste | Waste that does not pose a biological, chemical, radioactive, or physical hazard | Non-risk general waste
Notes: Infectious and anatomic wastes together represent the majority of hazardous waste, up to 15% of the total waste from health-care activities. Sharps represent about 1% of the total waste but they are a major source of disease transmission if not properly managed. Chemicals and pharmaceuticals account for about 3% of waste from health-care activities while genotoxic waste, radioactive matter, and heavy metal content account for around 1% of the total health-care waste.

## Slide 9: Definitions - 3
Type of Waste | Definition | Examples
Chemical waste | Waste containing chemical substances | Broken thermometers and blood-pressure gauges Disinfectants that are expired or no longer needed Film developer Laboratory reagents Pressurised containers Solvents Waste with high content of heavy metals, e.g., batteries
Radioactive waste | Waste containing radioactive substances | Contaminated glassware, packages, or absorbent paper Sealed sources Unused liquids from radiotherapy departments or laboratory research Urine and excreta from patients treated or tested with unsealed radionuclides
Notes: The use of radiation sources in medical and other applications is widespread throughout the world. Occasionally, the public is exposed to radioactive waste, which originates from radiotherapy treatment, that has not been disposed of properly.
It is noteworthy to note the Mercury use in healthcare settings such as thermometers and mercury sphygmomanometer because of the waste disposal issues.

## Slide 10: Sources - 1
 | Sharps | Infectious and pathological waste | Chemical, pharmaceutical and cytotoxic waste | General waste
Medical ward | Hypodermic needles, intravenous set needles; broken vials and ampoules | Dressings, bandages, gauze, and cotton contaminated with blood or body fluids; gloves and masks contaminated with blood or body fluids | Broken thermometers and blood pressure gauges; spilt medicines; spent disinfectants | Packaging, food scraps, paper, flowers, empty saline bottles, non-bloody diapers; non-bloody intravenous tubing and bags
Operating theatre | Needles, intravenous sets, scalpels, blades, saws | Blood and other body fluids; suction canisters; gowns, gloves, masks, gauze, and other waste contaminated with blood and body fluids; tissues, organs, fetuses, body parts | Spent disinfectants | Packaging, uncontaminated gowns, gloves, masks, hats and shoe covers
Laboratory | Needles; broken glass, Petri dishes, slides and cover slips; broken pipettes | Blood and body fluids; microbiological cultures and stocks; tissue; infected animal carcasses; tubes and containers contaminated with blood or body fluid | Fixatives; formalin; xylene, toluene, methanol, methylene chloride, and other solvents; broken lab thermometers | Packaging; paper, plastic containers
Pharmacy |  |  | Expired drugs; spilled drugs | Packaging, paper, empty containers
Radiology |  |  | Silver; fixing and developing solutions; acetic acid; glutaraldehyde | Packaging, paper
Notes: Healthcare waste has many potential sources. The major sources of health-care waste are:
    hospitals and other health-care establishments
    laboratories and research centres
    mortuary and autopsy centres
    animal research and testing laboratories
    blood banks and collection services
    nursing homes for the elderly.
High-income countries generate on average up to 0.5 kg of hazardous waste per hospital bed per day; while low-income countries generate on average 0.2 kg of hazardous waste per hospital bed per day. However, health-care waste is often not separated into hazardous or non-hazardous wastes in low-income countries making the real quantity of hazardous waste higher.

## Slide 11: Sources - 2
 | Sharps | Infectious and pathological waste | Chemical, pharmaceutical and cytotoxic waste | General waste
Chemotherapy | Needles and syringes |  | Bulk chemotherapeutic waste; vials, gloves and other material contaminated with cytotoxic agents; contaminated excreta and urine | Packaging, paper
Environmental Services | Broken glass |  | Disinfectants (glutaraldehyde, phenols, etc.), cleaners, spilled mercury, pesticides | Packaging, flowers, newspapers, magazines, cardboard, plastic and glass containers, yard waste
Engineering |  |  | Cleaning solvents, oils, lubricants, thinners, asbestos, broken mercury devices, batteries | Packaging, construction or demolition waste, wood, metal
Food services |  |  |  | Food scraps; plastic, metal and glass containers; packaging
Physicians’ offices | Needles and syringes, broken ampoules and vials | Cotton, gauze, dressing, gloves, masks and other materials contaminated with blood or other body fluids | Broken thermometers and blood pressure gauges; expired drugs; spent disinfectants | Packaging, office paper, newspapers, magazines, uncontaminated gloves and masks
Dental offices | Needles and syringes, broken ampoules | Cotton, gauze, gloves, masks and other materials contaminated with blood | Dental amalgam; spent disinfectants | Packaging, office paper, newspapers, magazines, uncontaminated gloves and masks
Home health care | Lancets and insulin injection needles | Bandages and other material contaminated with blood or other body fluids | Broken thermometers | Domestic waste

## Slide 12: Collection
Collect in containers that reduce the risk of exposure to users
Label with the international biohazard symbol
Do not overfill
Notes: Waste must be collected in containers that reduce the risk of exposure to users and meet minimum specifications. They should be labelled with the international biohazard symbol, and not overfilled. The biohazard label can be painted on the containers or self-adhesive labels can be used.

## Slide 13: Collection
Segregate from regular garbage
Place in special collection containers at the point of generation
  keep separate from other waste
Place labelled containers in areas where the specific waste is generated
  along with containers for general garbage
Non-infectious and non-hazardous waste should be disposed of with regular garbage, recycled, or composted, as appropriate
Notes: Segregation of healthcare waste from regular garbage should occur at all healthcare facilities.

## Slide 14: Collection Containers - 1
Type of Waste | Specifications for Container or Bag | Examples
Sharps | Container should be puncture-resistant, leak-proof on the sides and bottom, and durable. Container should have the biohazard label. Container should be closable for transport. | Empty bleach bottle with a biohazard label. Thick, rigid, puncture-resistant cardboard box with a biohazard label. Rigid plastic container with a biohazard label.
Non-sharps biomedical solid and semi-liquid waste | Plastic bag that is leak-proof; designed to prevent ripping, tearing, or bursting under normal use. The plastic bag should be placed inside a rigid container. Rigid container should be leak-proof, durable, labeled with the biohazard symbol, and red or yellow in colour. | Red or yellow plastic bags should be used. When coloured bags are not available, plastic bag with the biohazard label can be placed in a red or yellow-painted garbage can or dust bin.

## Slide 15: Collection Containers - 2
Type of Waste | Specifications for Container or Bag | Examples
Non-sharps biomedical liquid waste | Container should be leak-proof and durable. Container should be marked with the biohazard label if it will be used to transport waste. Container should be designed to be transported without spillage. | Bottles, vials, plastic containers, canisters, pails marked with biohazard labels.

## Slide 16: In-House Transport
Waste transporters should wear gloves
Cart for transporting healthcare waste within a facility should be fully enclosed
Health care waste carts should not be used for regular garbage
Notes: Carts should be cleaned and disinfected regularly.

## Slide 17: Storage
Minimise the impact of odours or putrescent waste
  Do not store for more than 3 days
  Putrescent waste should be transported to the landfill immediately and buried in special trenches
Be accessible to authorised employees only and lockable to prevent unauthorised access
Be protected from animals and not provide a breeding place or food source for insects and rodents
Kept clean and free at all times of any loose debris and standing water
Disinfect weekly and whenever a spill occurs
Notes: If storage of waste is necessary, the storage area (skip, shed, etc.) should meet the following parameters:
  Be protected from water, rain, or wind;
  Minimise the impact of odours, or putrescent waste (waste that can decompose and produce odours after several days). Do not store for more than 3 days; putrescent waste should be transported to the landfill immediately and buried in special trenches;
  Be accessible to authorised employees and lockable to prevent unauthorised access;
  Be protected from animals and not provide a breeding place or food source for insects and rodents; and
  Kept clean and free at all times of any loose debris and standing water. It should be disinfected weekly and whenever a spill occurs.

## Slide 18: Treatment and Off-Site Transport
The World Health Organization does not recommend use of campfire-style open-pit burning, burning in a cement firebox, burning in drums, or open-burn cement-block incinerators, which should be discontinued
Notes: A variety of methods are available to treat healthcare waste. A number of variables will dictate the treatment method, the primary one being economic resources. On-going research by organisations, such as the United Nations Global Environment Fund, World Health Organization, has provided a number of treatment technology options.
These treatment methods can be used in combination. Healthcare waste from outlying areas could be transported to a centralised facility.
Health centres may decide to bury blood-soaked material, small tissues, and placentas in small burial pits and transport sharps for disposal in special landfill trenches. This reduces the amount of waste being transported to the landfill and avoids the problem of storing putrescent waste for extended periods. Another approach is to use sharps disposal burial pits for needles, syringes, and items that may injure waste pickers and transporters; other waste such as blood-soaked material, can be picked up and disposed in special landfill trenches.

## Slide 19: Incineration
Small in-house incinerators, the local crematorium, and newer large-scale medical waste incinerators need to meet strict air pollution control requirements
Where possible, should be replaced by cleaner, state-of-the-art non-burn treatment technologies
Notes: These methods are inefficient at destroying pathogens and release high levels of toxic pollutants.

## Slide 20: Waste Treatment and Disposal Options - 1
Type of Waste | Methods | Notes
All infectious wastes Except cultures and anatomical parts | Packaging, transport, and treatment by incineration or non-burn technology. When no technology is available, burial in special landfill trenches | This method should be used by large facilities (e.g., hospitals).
All infectious wastes Except cultures and anatomical parts | Small on-site burial pits | This method could be used in health centres away from coastal areas and local wells, in areas that do not flood, and where the water table is at least 1.5 metres deeper than the bottom of the pit.
Notes: Incineration of waste has been widely practiced but inadequate incineration or the incineration of unsuitable materials results in the release of pollutants into the air and of ash residue. Incinerated materials containing chlorine can generate dioxins and furans, which are human carcinogens and have been associated with a range of adverse health effects. Incineration of heavy metals or materials with high metal content (in particular lead, mercury and cadmium) can lead to the spread of toxic metals in the environment. Dioxins, furans and metals are persistent and bio-accumulate in the environment. Materials containing chlorine or metal should therefore not be incinerated.
Only modern incinerators operating at 850-1100 °C and fitted with special gas-cleaning equipment are able to comply with the international emission standards for dioxins and furans.
Alternatives to incineration are available, such as autoclaving, microwaving, steam treatment integrated with internal mixing, and chemical treatment.

## Slide 21: Waste Treatment and Disposal Options - 2
Type of Waste | Methods | Notes
Cultures | Small on-site autoclaves or pressure cookers. | Preferably in the laboratory.
Anatomical parts | Interment at burial grounds or cemeteries. | This is the basic method for body parts.
Anatomical parts | Cremation. | ? use a local crematorium.
Placenta waste And small-tissue waste | Small on-site burial pits or interment at burial grounds or cemeteries. | These are acceptable methods.
Placenta waste And small-tissue waste | Composting method. | This is an acceptable method.

## Slide 22: Waste Treatment and Disposal Options - 3
Type of Waste | Methods | Notes
Free-flowing blood and body fluids | Sanitary sewer. When sanitary sewers are not available, known infectious blood and body fluids should be decontaminated with the addition of disinfectant such as sodium hypochlorite. | This method applies to all health facilities with sanitary sewers.

## Slide 23: Transport
Waste contained in sealed plastic bags and/or sharps containers
Place in hard corrugated cardboard boxes or reusable plastic bins for transport every few days (sooner for putrescent waste) or whenever sufficient waste has accumulated
Containers have biohazard labels or are colour coded
  e.g., red or yellow or as dictated by local legislation

## Slide 24: Management
Waste management should be incorporated into policies, procedures, and programmes to minimise the risk of spreading infection in and from the health care facility, thereby protecting patients, healthcare workers, and the public
Notes: All health care facilities should have a person or group responsible for healthcare waste and waste management plans. Waste management should be incorporated into policies, procedures, and programmes to minimise the risk of spreading infection in and from the health care facility, thereby protecting patients, healthcare workers, and the public.
A number of resources are available for developing a waste management programme using a Rapid Assessment Tool available from the World Health Organization. This tool can provide an overview of the strengths and weaknesses of a waste management program and provide direction for further planning and implementation stages:
http://www.who.int/entity/injection_safety/toolbox/en/Healthcarewastemanagementtool.xls
Various programs from the Safe Injection Global Network offer useful guidance especially “Procuring Single-use Injection Equipment and Safety Boxes”.

## Slide 25: Training
Initial training emphasise safe healthcare waste management practices
Practical training provided to all those involved in handling, packaging, transporting, and disposing of health care waste.
Notes: A training programme should be used to present the elements of a plan and begin its implementation. Initial training could emphasize safe health care waste management practices and address issues related to the comprehensive, long-term plan. Practical training should be provided to all those involved in handling, packaging, transporting, and disposing of health care waste.

## Slide 26: References
Healthcare waste, World Health Organization http://www.who.int/water_sanitation_health/healthcare_waste/en/
MedWaste Treatment – Minimizing Harm, Maximizing Health 2003. Health Care without Harm. http://www.bvsde.paho.org/bvsacd/cd43/mer.pdf
UN Global Environmental Fund (GEF) Global Healthcare Waste Project. http://www.gefmedwaste.org
World Health Organization: Safe Injection Global Network. http://www.who.int/medical_devices/collaborations/network/en/

## Slide 27: Quiz
The majority of hazardous healthcare waste includes the following types:
  Sharps and Infectious
  Infectious and Pathological
  Chemical and Infectious
  Infectious and Pharmaceutical
Waste containers must:
  Have a biohazard label
  Not be overfilled
  Not pose a risk
  All of the above
The type of treatment for healthcare waste depends primarily on:
  Economic resources
  Transportation options
  Available landfills
  All of the above
Notes: B
D
A

## Slide 28: International Federation of Infection Control
IFIC’s mission is to facilitate international networking in order to improve the prevention and control of healthcare associated infections worldwide. It is an umbrella organisation of societies and associations of healthcare professionals in infection control and related fields across the globe .
The goal of IFIC is to minimise the risk of infection within healthcare settings through development of a network of infection control organisations for communication, consensus building, education and sharing expertise.
For more information go to http://theific.org/